For 2 packets, ~ D_{2 packets} = d_{end-end} `+` d_{queue of bottleneck}, newline newline d_{queue of bottleneck} = L_1 over R_1 newline newline L_1 over R_1 ~=~ 4000 over (5 cdot 10^7) newline newline L over R ~=~ 1.24 cdot 10^-4 seconds newline newline font sans bold [D_2packets = 2.5173 cdot 10^-4 seconds]
For 1 packet, ~ D_i = d_queue + d_trans + d_propa ~ , d_queue = 0 newline newline D_{end-end} = D_{1} + D_{2} + D_{3} newline newline D_{end-end} = (d_trans1 + d_propa1) + (d_trans2 + d_propa2) + (d_trans3 + d_propa3) newline newline L_1 over R_1 + S_1 over c ~+~ L_2 over R_2 + S_2 over c ~+~ L_3 over R_3 + S_3 over c newline newline 4000 over (5 cdot 10^7) + 100 over (3 cdot 10^8) ~+~ 4000 over (1 cdot 10^9) + 1000 over (3 cdot 10^8) ~+~ 4000 over (5 cdot 10^8) + 20 over (3 cdot 10^8) newline newline d_{end-end} `=` 1.2773 cdot 10^-4 seconds
4000 over (5 cdot 10^7) + 100 over (3 cdot 10^8) ~+~ 4000 over (2.5 cdot 10^7) + 1000 over (3 cdot 10^8) ~+~ 4000 over (5 cdot 10^8) + 20 over (3 cdot 10^8) newline newline d_{end-end} `=` 2.8373 cdot 10^-4 seconds ~,~ d_{queue of bottleneck} = L_1 over R_1 newline newline L_1 over R_1 ~=~ 4000 over (5 cdot 10^7) `=` 1.6 cdot 10^-4 newline newline font sans bold [D_2packets = 4.4373 cdot 10^-4 seconds]
N = R cdot RTT over L = (500 Mbps cdot 0.02 sec) over (8000 bits) = 1 cdot 10^7 over (8000 bits) = bold( 1250 packets)
(Bits delivered [0,T])over(T=Time elapsed) = (T over (L / R) cdot L) over T ~=~ bold R newline newline Thruput ~=~ R ~=~ 1 Gbps ~=~ bold (1 cdot 10^9 bits per second) newline newline Thruput = R over L = (1 Gbps) over (8kb)= 125000 = bold (1.25 cdot 10^5 pkts/sec)
Caleb Faruki
Dr. Xiaolan Zhang
CISC4615 Data Comm & Networks
October 30, 2013

Homework 4

1a

1b

2
Max throughput is the average rate of data delivery to the destination. Throughput is constrained by the transmission rate of the bottleneck link. Data can't be propagated until it is transmitted in full. A link transmits 1 packet at a time and propagates 1 packet at a time.

The bottleneck link transmits packets slower than all other links. Links after the bottleneck can't transmit/propagate a packet until a packet is received from the bottleneck. This means that even if another link can transmit faster, packets may only be sent as fast as they are received.

3
Thruput of rdt3.0: / L = 8kb (8*103) / R = 1Gbps (1*109) / RTT = 20ms (2*10-3) / dACKtrans = 0 / dqueue, dproc = 0

Find window size N for: / Thruput = 500 Mbps	Window size = N = 1250

4
See attached photo for solution.